## Slide 1
Sectors | Behind the meter | Below the substation | On the bulk grid
Residential | Wall-mounted batteries EVs Water heaters* | Neighborhood batteries Public & Workplace parked EVs (grouped because typically on the same feeders) | Garage batteries EVs Water heaters
Commercial | Pad-mounted batteries EV fleets Latent/sensible heat* (grouped because similar options) |  | Garage batteries EVs Water heaters
Industrial |  | MV/LV side storage (“below” the transformer) | Garage batteries EVs Water heaters
+ distribution costs (wires + bins-on-poles)
+ substation + transmission costs
*Heat storage does not allow feeding back onto the grid
LCOE+ LCOS

## Slide 2
+ distribution costs (wires + bins-on-poles)
+ substation + transmission costs
LCOE+ LCOS
Solar+V2L
Solar+BESS
Solar+V2G
Solar+BESS

## Slide 3
 |  | Primarily discharges to |  | 
 |  | Local load | Distribution poles | Bulk system
Primarily charges from | Local supply | Co-location Home batteries w/ rooftop solar, Remote worker EVs, behind-the-fence industrial w/ supply. | Supply socialization Parking lot battery at the school charging in day and feeding the borough at night. | Hybrid generation Hybrid solar/wind/run-of-river-hydro+BESS plants; behind-the-fence industrial.
 | Distribution poles | Neighborly aid Garage batteries drawing in daytime to power the kettle. | Feeder balancing Coop/utility battery soaking midday solar for evening dispatch. | Postcode power plant Utility-scale battery feeding back local oversupply to bulk.
 | Bulk system | Peak-shaving Behind-the-fence industrial battery trickle-charging to avoid demand charges. | Congestion relief Substation battery fed by far-off supply dispatching when load > power line capacity. | Bulk firming Big utility battery for spatiotemporal arbitrage of supply and demand.